GP8B
Datasheet
-
Version 5.x

Copyright (C) 2020 Guillaume Guillet
Licensed under CERN-OHL-W v2 or later

This source describes Open Hardware and is licensed under the CERN-OHL-W v2 or later.

You may redistribute and modify this documentation and make products using it under the terms of the CERN-OHL-W v2 (https:/cern.ch/cern-ohl). This documentation is distributed WITHOUT ANY EXPRESS OR IMPLIED WARRANTY, INCLUDING OF MERCHANTABILITY, SATISFACTORY QUALITY AND FITNESS FOR A PARTICULAR PURPOSE.

Please see the CERN-OHL-W v2 for applicable conditions.

# Description
The GP8B or G_Processor8Bits is a home-made, from scratch, with no micro-controller, only made with logic circuits, 8bits processor.
The goal of this project is to create an 8bit computer community with the help of custom mecanical and electronic standards to build a nice and compatible environnement.
## Features
- 64 kByte of RAM maximum.
- Using ALUminium*1 in a CPLD for an 8bits ALU (arithmetic-logic unit).
- A simple SPI implementation.
- 16 writable bits for peripheral communication.
- 16 readable bits for peripheral communication.
- Following the custom standard SPS1*2.
- Following the CodeG binary rev1 standard.
- Accessible debug pins and Jtag for the CPLD.
- 50Mhz theorical maximum frequency.

*1 ALUminium is an VHDL 8bits ALU code that you can find here :
https://github.com/JonathSpirit/ALUminium
*2 You can find SPS1 standard here :
https://github.com/JonathSpirit/GComputer_standard

# CodeG
GP8B execute the revision 1 of the homemade binary language called CodeG :
CodeG binary revision 1.0
Instruction selection
Opcode	Hex	Name	Description
xxx0’0000	0x00	BWRITE1_CLK	Apply value to bus “write 1”.
xxx0’0001	0x01	BWRITE2_CLK	Apply value to bus “write 2”.
xxx0’0010	0x02	BPCS_CLK	Apply value to bus “peripheral CS”.
xxx0’0011	0x03	OPLEFT_CLK	Apply value to the left operation.
xxx0’0100	0x04	OPRIGHT_CLK	Apply value to the right operation.
xxx0’0101	0x05	OPCHOOSE_CLK	Apply value for choosing the operation.
xxx0’0110	0x06	PERIPHERAL_CLK	Send a clock pulse to the peripheral.
xxx0’0111	0x07	BJMPSRC1_CLK	Apply value to bus “jump source 1”.
xxx0’1000	0x08	BJMPSRC2_CLK	Apply value to bus “jump source 2”.
xxx0’1001	0x09	BJMPSRC3_CLK	Apply value to bus “jump source 3”.
xxx0’1010	0x0A	JMPSRC_CLK	Jump to the address of “jump source”.
xxx0’1011	0x0B	BRAMADD1_CLK	Apply value to bus “RAM address 1”.
xxx0’1100	0x0C	BRAMADD2_CLK	Apply value to bus “RAM address 2”.
xxx0’1101	0x0D	SPI_CLK	Send a clock pulse for the SPI.
xxx0’1110	0x0E	BCFG_SPI_CLK	Apply value to the config bus SPI.
xxx0’1111	0x0F	STICK	Simple tick, do nothing (delay).
xxx1’0000	0x10	IF	Conditional instruction.
xxx1’0001	0x11	IFNOT	Conditional instruction inverted.
xxx1’0010	0x12	RAMW	Write value to the actual address of the memory.
xxx1’0011	0x13	UOP	Undefined operation.
xxx1’0100	0x14	UOP	Undefined operation.
xxx1’0101	0x15	UOP	Undefined operation.
xxx1’0110	0x16	UOP	Undefined operation.
xxx1’0111	0x17	LTICK	Long tick, do nothing (delay).

CodeG binary revision 1.0
Argument selection
Opcode	Hex	Name	Description
000x’xxxx	0x00	SRCVALUE	The value stored to the source.
001x’xxxx	0x20	BREAD1	The value of the read bus 1.
010x’xxxx	0x40	BREAD2	The value of the read bus 2.
011x’xxxx	0x60	OPRESULT	The value of the operation result (ALU).
100x’xxxx	0x80	RAMVALUE	The value of the processor memory.
101x’xxxx	0xA0	SPI	The value of the SPI.
110x’xxxx	0xC0	EXT_1	External value 1.
111x’xxxx	0xE0	EXT_2	External value 2.

# Blocks details
## Bus
Details of essential/fonctionnal bus are listed here :
Bus name	Size (bits)	Direction	Description
BWRITE1	8	out	Bus for external peripheral communication.
A D-latch chip control the write bus 1. / You can apply a value with the instruction “BWRITE1_CLK”.
BWRITE2	8	out	Bus for external peripheral communication.
A D-latch chip control the write bus 2. / You can apply a value with the instruction “BWRITE2_CLK”.

Bus name	Size (bits)	Direction	Description
BREAD1	8	in	Bus for external peripheral communication.
The readable bus 1 can be directly applied as an argument into the “NUMBER” bus.
BREAD2	8	in	Bus for external peripheral communication.
The readable bus 2 can be directly applied as an argument into the “NUMBER” bus.
NUMBER	8	in/out	Main argument bus.
The “NUMBER” bus is applied almost everywhere. With it, you can control most of the register like the writeable bus 1 or 2.

NUMBER	8	in/out	Main argument bus.
You can choose the value that goes into the “NUMBER” bus by changing the last 3bits of the instruction code. / You can choose 8 differents value : / - The source. / - BREAD1 / - BREAD2 / - Operation result / - RAM / - SPI / - External bus 1 / - External bus 2

## Instruction execution
### Sequencer
The first main component is a 4bits counter that will receive the “GLOBAL_CLK” of the motherboard.
The goal of this chip is to provide, with the help of a demux, all the pulse required for executing instruction sequentially.

The 4bits count from 0 to 4, the fifth clock reset the counter to 0:

Every pulse from the sequencer represent a stat/action:

Sequence value	Action/Stat	Counter reset?	Next address?	Instruction latched?
0	Sync bit	No	No	No
At this stat, no instruction are executed and the SYNC_BIT is pulled high, this serve only for syncing with an interface like a debugger and prepare the execution of the next instruction.
1	Instruction set	No	Yes	Yes
A pulse have been made to ‘U7’ (8bit D-Latch) to save the instruction to execute and the next address is requested (the argument).
2	Execution	Yes/No	Yes/No	No
“Simple instruction”: One pulse is made to execute the instruction and a reset/next address is requested. / “Complex instruction”: The first part of the instruction is executed with no reset: / IF/IFNOT: If the argument is valid (>0 or =0), then the next instruction is skipped (usually a JMPSRC_CLK instruction) by requesting the next address. / RAMW: The “output enable” pin is pulled high for write preparation. / Noting is executed for UOP/LTICK instructions.
3	Waiting	No	No	No
At this stat, the processor do nothing (this stat is only useful for write preparation to the memory).
4	RAM Write or END	Yes	Yes	No
Depending on the instruction: / RAMW: The RAM write the requested data by pulling low the “write enable” pin. / At the end, a reset and the next address is requested.

### Simple instructions
Simple instruction consist of just one pulse and an argument.
Every simple instruction is executed in 3 rising-edges from GLOBAL_CLK.

Opcode	Hex	Name	Description
xxx0’0000	0x00	BWRITE1_CLK	Apply value to bus “write 1”.
xxx0’0001	0x01	BWRITE2_CLK	Apply value to bus “write 2”.
xxx0’0010	0x02	BPCS_CLK	Apply value to bus “peripheral CS”.
xxx0’0011	0x03	OPLEFT_CLK	Apply value to the left operation.
xxx0’0100	0x04	OPRIGHT_CLK	Apply value to the right operation.
xxx0’0101	0x05	OPCHOOSE_CLK	Apply value for choosing the operation.
xxx0’0110	0x06	PERIPHERAL_CLK	Send a clock pulse to the peripheral.
xxx0’0111	0x07	BJMPSRC1_CLK	Apply value to bus “jump source 1”.
xxx0’1000	0x08	BJMPSRC2_CLK	Apply value to bus “jump source 2”.
xxx0’1001	0x09	BJMPSRC3_CLK	Apply value to bus “jump source 3”.
xxx0’1010	0x0A	JMPSRC_CLK	Jump to the address of “jump source”.
xxx0’1011	0x0B	BRAMADD1_CLK	Apply value to bus “RAM address 1”.
xxx0’1100	0x0C	BRAMADD2_CLK	Apply value to bus “RAM address 2”.
xxx0’1101	0x0D	SPI_CLK	Send a clock pulse for the SPI.
xxx0’1110	0x0E	BCFG_SPI_CLK	Apply value to the config bus SPI.
xxx0’1111	0x0F	STICK	Simple tick, do nothing (delay).

### Complex instructions
Complex instructions are instructions that takes 5 rising-edges from GLOBAL_CLK to execute.

Opcode	Hex	Name	Description
xxx1’0000	0x10	IF	Conditional instruction.
xxx1’0001	0x11	IFNOT	Conditional instruction inverted.
xxx1’0010	0x12	RAMW	Write value to the actual address of the memory.
xxx1’0111	0x17	LTICK	Long tick, do nothing (delay).

The RAMW instruction consist by pulling OE low when counter is at 2, and send a WE pulse when counter is at 4.
The conditional instruction consist of checking the argument when counter is at 2, if the argument is valid, the next instruction (usually a jump) is skipped else the next instruction is executed.

## Arguments

The argument for an operation is selected by changing the last 3bits of the opcode :

The 3bits, once latched, are connected to the demux “U17”.

Every “SELECTING” line control a 8bits buffer with tri-state output and every buffer is connected to the argument bus “NUMBER”.

Opcode	Hex	Name	Description
000x’xxxx	0x00	SRCVALUE	The value stored to the source.
001x’xxxx	0x20	BREAD1	The value of the read bus 1.
010x’xxxx	0x40	BREAD2	The value of the read bus 2.
011x’xxxx	0x60	OPRESULT	The value of the operation result (ALU).
100x’xxxx	0x80	RAMVALUE	The value of the processor memory.
101x’xxxx	0xA0	SPI	The value of the SPI.
110x’xxxx	0xC0	EXT_1	External value 1.
111x’xxxx	0xE0	EXT_2	External value 2.

# Fabrication
## Getting the PCB
Fabrication files can be found in the folder : “documents/GP8B_gerbert”.

For JLCPCB, you can zip the fabrication folder and send it to them directly.

## Getting the materials
A bill of materials can be found here : “documents/GP8B_materials”. Note that if you want to change the supplier, you have to make sur that the component is fully compatible mostly for the package.

## Soldering
If you solder the board manually, a microscope can be useful for small component like the CPLD.
Follow the bill of materials and the PCB placement file to solder the board.

# Changes
Revision 0:
initial release